How to check your engine oil…

Hi I am Peter from Parts Plus and today we are going to look at how to check your engines oil level which is a crucial part of maintaining your car.

This will only take a few minutes and is something that should be done on a regular basis. Please follow these steps;

STEP 1

First make sure the car is on level ground, also if the engine has been running switch it off and  wait a few minutes for the oil to settle in the bottom. These things will allow you to get an accurate oil reading.

STEP 2

Now open the bonnet, the release is usually under the dash on the drivers’ side (if you can’t find it refer to your vehicles manual in the glove box). Once the bonnet is open look for the engine dipstick. It usually has a yellow handle but not always.

STEP 3

Remove the stick and wipe the excess oil off with a paper towel or rag. Look at the stick, it usually has a couple of marks an add mark which is closest to the bottom and a full mark which is slightly above the add mark.

Re dip the stick pull it out and have a close look and you will see where the oil level is up to on the stick. If you need oil, unscrew the oil cap on top of the motor and add oil ,a couple of hundred millilitres, allow a couple of minutes for the oil to settle in the bottom of the motor and go through the process of checking the oil level again, repeat these steps until the oil reaches the full mark.

REMEMBER

This is something that should be done on a regular basis, all engines use oil but every vehicle is different, I check my oil every couple of weeks or 800-1000 kms so start off by checking it weekly it only takes a few minutes.

Also if you are towing or driving on a trip you will need to check the oil more regulary and always refer to the owners manual.

Thanks for taking the time to watch this Parts Plus presentation….